## Slide 1: Advanced Encryption Standard Implementation on a Field Programmable Gate Array Development Board
By: CDT Matteo Cordray

## Slide 2
Overview
System Design
AES
UART
Current Progress
What’s Next
Agenda

## Slide 3
Overview
Why AES?
Why on an FPGA?
Why this project?

## Slide 4
Overview – Why this project?
Ultimately: Modern computers need secure hardware
Communication Systems
Data Storage Centers
Transportation
First learned about AES during CY450 class…

## Slide 5
Overview – Why on an FPGA?
Type | Cost | Efficiency / Speed | Flexibility
Microcontroller | <$5 p.u. | Can run semi-concurrent tasks (FreeRTOS). Efficient, but not as fast as an average FPGA (20 MHz). | Easy to purchase individual chip, can connect any peripheral you’d like. However, easier to stick with common protocols.
FPGA | ~$100-$1k p.u. | Only one task – efficient and fast hardware. (550 MHz max). | Typically stick to what’s on development board. But overall can change whatever you want.
ASIC | $100k - $1m p.u. | Only one task – very efficient and fast hardware. | Configuration cannot change.
FPGAs provide the most flexibility, with tradeoffs in cost and efficiency.

## Slide 6
Overview – The De1-SOC Board
Used development board’s soft processor during Computer Architecture course (EE375).
Benefits
  Easy to program through Intel Quartus Software.
  Easy to obtain through EECS department.
Drawbacks
  Documentation lacks explanations, and example code is hard to find compared to newer FPGA’s on the market.
  Half of the space is taken up by a soft-core processor, which makes the general size of the development board quite large.

## Slide 7
System Design - Encryption
Goal for the design is to showcase a simple, yet effective demonstration of the successful operation of AES on a single FPGA.
Hello, World!
Encryption
dQEPBnxXBxzosDldimjK1w==

## Slide 8
System Design - Decryption
Goal for the design is to showcase a simple, yet effective demonstration of the successful operation of AES on a single FPGA.
Decryption
dQEPBnxXBxzosDldimjK1w==
Hello, World!

## Slide 9
System Design - Connections
Connections - Encryption
USB-Serial Cable
Serial Connection
Hello, World!

## Slide 10
System Design - Connections
Connections - Encryption
UART (TX, RX)
Pin 0, 1 on Arduino
GPIO Pin 25, 26 on FPGA
Serial Connection
Hello, World!
Serial Connection
dQEPBnxXBxzosDldimjK1w==

## Slide 11
System Design - Connections
Connections - Decryption
UART (TX, RX)
Pin 0, 1 on Arduino
GPIO Pin 27, 28 on FPGA
Serial Connection
Serial Connection
dQEPBnxXBxzosDldimjK1w==
Hello, World!

## Slide 12
System Design - Connections
Connections – Whole System
Hello, World!
Hello, World!
dQEPBnxXBxzosDldimjK1w==
Encryption
Decryption

## Slide 13
AES – Advanced Encryption Standard
What is AES?
Why AES?
The Advanced Encryption Standard was one of the most successful implementation taught in CY450.
  The CY450 class is where project idea originated.
Benefits
  AES lets you choose key sizes, whereas others such as DES have a fixed key length (56-bit key).
Negatives
  Security is still dependent on key size.

## Slide 14
AES – How it Works
Substitute Bytes
  Uses a table (S-Box) to perform byte-by-byte substitutions
Shift Rows
  Permutation by row
Mix Columns
  A substitution that alters each byte in a column as a function of all the bytes in the column
Add Round Key
  Bitwise XOR of the current block with a portion of the expanded key
*Slide taken from CY450 – Lesson 17 –Cryptography I ppt

## Slide 15
AES – How it Works
*Slide taken from CY450 – Lesson 17 –Cryptography I ppt
AES S-Box
If my input is 0x95..
Then my output is 0x2A

## Slide 16
AES – Test Bench Code
Compare output of AES from plaintext to ciphertext

## Slide 17
AES – Test Bench Simulation
Add Round Key
S-Box
Block (shift, etc)
Clock Cycle

## Slide 18
UART – Universal Asychronous/Synchronous Transmitter
What is UART?
Why UART?
The UART Protocol is a Protocol designed to serially communicate between two clients using only two wires
  Other implementations include RS-232, SWD, etc.
Benefits
  Easy to interface with Arduino IDE and the Arduino Framework using an Arduino Uno.
  Asynchronous mode does not require a clock line.
Negatives
  Communication is slower than SPI, or other high-speed protocols.

## Slide 19
UART – Testbench Code
Sends a bit through the transmit line and verifies the bit is received on the receive line.
Simple to test in testbench.

## Slide 20
UART – Testbench Simulation
Clock for testbench, not UART
These results match, so we get a success message
Takes around 150 ns to finish job…something to consider

## Slide 21
Current Progress
Not fully up to date, but GitHub website contains code on a public repository documenting my journey learning Verilog.
Point to resources used throughout the project.
For future -> Add current UART + AES code and links to sources on GitHub.

## Slide 22
Current Progress - UART

## Slide 23
What’s next?
Long range goal: Complete full implementation to send to eFabless Caravel Project.
Short range goal: Prove system works on FPGA with Arduino’s to display output.
Integrate UART and AES capability with two Arduino’s for encryption.
Integrate UART and AES capability with two Arduino’s for decryption.
Combine encryption and decryption parts together.
Connect three Arduino’s to prove system works.

## Slide 24
AES and UART code respositories
AES: secworks/aes: Verilog implementation of the symmetric block cipher AES (Advanced Encryption Standard) as specified in NIST FIPS 197. This implementation supports 128 and 256 bit keys. (github.com)
UART: varmil/uart-verilog: the UART module with Quartus Prime (github.com).

## Slide 25
Questions?